## Slide 1: Quick update about Trip to Elvia in France
Visited Elvia PCB shop in Coutances, France and worked with in house engineer to study the production of laser etched ZZ PCB’s (Laser etching is normally used as a post-process for cleaning chemically etched copper edges, and for trimming PCB’s). We want to use laser ablation as the primary method for cutting into the copper.
We laser etched many ZZ patterns into sample substrates (50um FR4 with 5um Cu), and varied a number of parameters like the laser power, the number of passes of the laser over the pattern, etc.
Laser can generate pattern on an area of about 500mm x 600mm
Surprisingly it only takes a few minutes (depending on the number of passes) to generate a ZZ pattern on a ~10cm x ~10cm area!
Gap width determined by laser x-sect profile (circle w/ diam. <25um)
We made our gap width equal to the laser profile, but needed to make several (4-8) passes to fully cut through the copper (the precision of the XY translation is at the level of a few um so that the laser retraces over its path very accurately
Do the shorts we found in earlier PCB’s depend on the ZZ parameters (eg stretch or ZZ-period)?

## Slide 2
First iteration of laser etched ZZ PCB showed ~20% of pads shorted to neighbor
When we made these new iterations, there were virtually no shorts found in any of the patterns
  We only found a few shorts in those patterns where we expected some (ie, ones where the laser stopped a little short of crossing at the ZZ tips)
  We also made “X” intersection points at the ZZ tips to diagnose the issues
  Some “X’s” were “incomplete”, some were exaggerated so we could study the behavior of the laser intersection point
  In some of the incomplete “X’s”, there were shorts (2-4 total out of ~100); in the exaggerated ones, they were all shorted, as expected (diagnostic test)
  For the regular “V” intersection, no shorts were found (maybe 1 or 2), but this may have been because the lines making the “V” did not overlap enough (the “X” precludes this possibility)
  For slightly “over-drawn” tip all shorts disappeared altogether
  For our earlier PCB, made last year, we were able to recover 13 of 14 shorts by exposing the PCB to a sulfuric acid bath (6 of those shorts returned)
    Maybe we washed away some debris that deposited during cutting, then some more got loose and got caught in trench???
Design of incomplete “X”
Cu not cut all the way through

## Slide 3
  We never found out why those shorts were there to begin with (no clues from the microscope – we indeed see some “junk” in the gap btwn shorted strips, but this junk is regularly present btwn strips that are not shorted as well)
  For the recently made ZZ patterns, we saw that some of the shorts were made by the fact that the laser simply did not cut all the way to the ZZ tip.
  Seems like we need a minimum of 4 loops to cut through the copper; too many loops creates a trench in the substrate that is many times deeper than the trench is wide (which is bad due to charge up & extra debris from production)
  Too many laser passes also creates thermal stress, so need to compromise with power and number of loops (ie, passes of the laser); should also consider Cu thickness as another parameter to tune.
  Must keep in mind idiosyncrasies of the machine: 4cm x 4cm patch of the patterns is cut at one time
  Elvia is getting a new dual-head laser (266nm + CO2(IR)) machine early next year, with higher cutting and positional precision (precision was already very good: +/-10um level), also can auto-load PCB’s fast production!
  Made some “diamond” 2-D ZZ-patterns too; generated array of micro-vias onto existing diamond structures without using position calibration tool and alignment was good to within few tens of um!!
  CONCLUSION: this process has a lot of potential for generating ZZ patterns with features not before attainable using chemical etching and should be pursued.
Micro-vias